Inspection Procedure for Safety Recall 16V413

STEP #1

Park the truck on a hard level surface, free of hazards, with enough room to move the main chute all the way to the right.

Move the main chute all the way to the right and as far up as possible (as shown in FIG A) without hitting any part of the truck or other objects. Once the chute is in position, set the parking break, and turn the engine off.  If your shop has other safety guidelines please flow them.

Now that the chute race is in the correct inspection position, and all safety measures in place, go to step #2.

STEP #2

Stand next to the road side front fender (as shown by the red arrow in FIG. A), and visually inspect both outside pivot supports, shown in FIG B.  View the underside of both of the pivot supports to check for the presence of a “KDF” tag welded to the bottom side of either of the pivot supports.

- If a “KDF” tag is present on either of the pivot supports, as shown in FIG. C, then the vehicle is subject to the recall, and will need to have the main chute race assembly replaced.

- If a “KDF” tag is not present on either of the pivot supports, then proceed to step #3.

STEP #3

If neither of the pivot supports have a “KDF” tag present, the race retaining angle will need to be examined.  The race retaining angle is shown in FIG. D and FIG. E.

- If the race retaining angle is rounded edge, as shown in FIG. F, then the vehicle is subject to the recall, and will need to have the main chute race assembly replaced.

- If the race retaining angle has a sharp edge, as shown in FIG. G, the vehicle is not subject to the recall.

# Text boxes

FIG. A

FIG. C

FIG. B

FIG. E

FIG. D

FIG. F

Rounded edge on race retaining angle

FIG. G

Sharp edge on race retaining angle