Models Affected:

Certain 2017 model year Winnebago View® and Itasca Navion® motorhomes with Truma Water Heater.

These vehicles were manufactured November 16, 2015 through June 23, 2016.

Tools Required:

- Cleaning rag

- Non-petroleum based cleaner

- Caulk gun

- Polyurethane-based sealant or equivalent to Winnebago part number 185987-03-02A.

Procedure:

- Wipe area clean around water heater grommet with a non-petroleum based cleaner and a clean rag.

- Apply Polyurethane-based sealant to area around water heater grommet.

# Text boxes

Not Sealed

Sealed